## Slide 1: Driver Drowsiness Detection System
Beginner-Friendly Overview
How the system detects sleepiness using AI + Camera
Mamona Sadaf – Research And Devolpment
Minahel Ahsan – Simulation and Algorithms
Sarah Omer – Embedded and Hardware

## Slide 2: System Goal
Monitors driver face in real time
Detects sleepiness indicators
Warns driver before danger
Works day & night

## Slide 3: How System Sees the Driver
Infrared (IR) camera captures face
Facial points detected using AI
Works even in darkness

## Slide 4: Detecting Eye State
Eye region cropped & stabilized
AI model classifies OPEN vs CLOSED
Long closure → Sleepiness detected

## Slide 5: Detecting Yawning
Measures mouth opening width
Large sustained opening = Yawn
Frequent yawns = fatigue

## Slide 6: Temporal Filtering
Blinks are fast, yawns are slow
Checks how long eyes/mouth stay closed/open
Reduces false alarms

## Slide 7: Alarm Activation
Triggers sound alert
Screen shows: Normal, Yawning, Drowsy
Helps prevent accidents

## Slide 8: Algorithms
MediaPipe Face Mesh – landmark detection
ROI Correction – stable eye region
CNN – eye open/closed classification
MAR – mouth opening measurement
Temporal Logic – blink vs microsleep
The pipeline works by detecting precise facial landmarks (MediaPipe) → stabilizing the eye region (ROI Correction) → classifying eye state (CNN) → measuring yawns (MAR) → using timing rules (Temporal Logic) to decide real drowsiness vs normal behaviors.

## Slide 9: MediaPipe Face Mesh
468 facial landmarks
Robust in low light
Handles head movement

## Slide 10: CNN Eye Classification
Learns eye patterns
More robust than geometric methods
Handles IR images and glasses

## Slide 11: Mouth Aspect Ratio (MAR)
Geometric yawn detection
Lightweight & fast
No extra CNN required

## Slide 12: Prototype

## Slide 13: Jetson Nano Integration Issues
Limited 4GB RAM
Heavy GPU load from AI models
Thermal throttling
Lower FPS under load
IR noise affects landmarks

## Slide 14: Final Summary
Multi-stage AI pipeline
Accurate day/night drowsiness detection
Embedded optimized (Jetson Nano)
Reliable & real-time